## Slide 1: The Optimal Method for ECG Printing Applications
Charles Spontelli – Bowling Green State University
William B. Birkett – Doppelganger, LLC

## Slide 2: Calibration Methods
TVI/SCTV
  Use Curves to match prescribed tonality of process colors
Near Neutral
  Use Curves to match prescribed gray balance and tonality
Color Management
  Use Color Management to match an ICC Profile
Optimal Method
  Use Curves to match an ICC Profile
Notes: TIMING 1.5 MINUTES
*This is an IMPORTANT slide as per Mark S.
The Optimal Method is a new print calibration method especially suited to ECG printing.
Review the various calibration methods.
The ASSUMPTION of TVI/SCTV is that if you match the individual CMYK TVI of Reference all the other colors fall into place and match.
The ASSUMPTION of NN or G7 is that if you match the prescribed grays all the other colors fall into place and match.
CM uses CM 3-D color transforms to match an ICC Profile.
The optimal method uses curves to match an ICC profile.
You could say it is a hybrid method, since it uses curves and color management technology.

## Slide 3: How It Works
Reduce overall color difference (∆E) between printing and an ICC Profile
Reduce Color Difference
∆E00
Print
Measurements
ICC Profile
Notes: TIMING 1 MINUTE
Hundreds of measurements of the precompensated fingerprint press run are on the left.
Corresponding measurements of the reference profile are on the right (CRPC6).
CURVES are adjusted to minimize the overall color difference.
OM uses data from HUNDREDS OF SAMPLES including grays to compute curves that minimize the color difference between the printing and reference profile.
The next two slides will show this in detail.

## Slide 4: How It Works
Iterative software loop
Stops when the overall color error (∆E) can’t be reduced any further (Optimal)
1
2
3
4
5
6
Print a test chart with standard inks and color gamut. Measure the samples.
Begin with Linear Curves (identity function).
Calculate reference L*a*b* values using the reference profile.
Calculate the color error (∆E) for each selected sample.
Adjust curve parameters to reduce overall color error of selected samples.
Repeat until overall color error (∆E) can’t be reduced any further
Print a test chart with standard inks and color gamut. Measure the samples.
Begin with Linear Curves (identity function).
Calculate reference L*a*b* values using the reference profile.
Calculate the color error (∆E) for each selected sample.
Repeat until overall color error (∆E) can’t be reduced any further.
Adjust curve parameters to reduce overall color error of selected samples.
Notes: TIMING 3 MINUTES
Here is an annotated flow chart showing how the Optimal method works.
The OM is an iterative process – Software Loop.
The curve parameters are adjusted in an iterative software loop. These are software iterations NOT press runs, as you will see animated in the next slide.
1 It begins with an uncalibrated (pre-compensated fingerprint) press run with solids that aim to match the reference profile.
2 The process begins with LINEAR curves.
3 The reference L a b values are calculated from the input CMYK values.
4 The difference ∆E between the printing and Reference.
5 Mathematic Optimization adjusts Curves to lower the overall ∆E for ALL samples!
6 Repeats until the overall ∆E can’t be reduced any further.
The next slide is a demonstration of the curve creation.

## Slide 5: Animation
Each frame shows an iteration or loop
Stops when overall color difference is Lowest (OPTIMAL)
That took 145 iterations for this example
Notes: TIMING 1 MINUTE `
This is an animation of what the OM is doing in each loop/iteration.
Each new set of curves (each frame) lowers the overall error ∆E between printing and profile.
The process STOPS at the LOWEST / OPTIMAL error.
The overall ∆E between printing and ICC Profile reference cannot be any lower.
This is the closest match this process can get to a reference profile. This took 145 iterations.

## Slide 6: Optimal Method Properties
Color reference is an ICC profile
Printing process can have any number of inks
Calibration test chart can use any sample set
Minimizes color errors for the sample set
Makes smooth vector curves from rough data
Ideal calibration technique for ECG printing
Notes: TIMING 1 MINUTE
As you’ve just seen, the Optimal Method is very different from other calibration techniques.
Please take a minute to read this list of its key properties (allow 20 seconds).
The rest of this presentation is about using the Optimal Method in ECG applications.
There are various approaches to implementing ECG, but all of them use color management at some level.
Bill will now discuss a simple technique for calibrating a classic color-managed workflow, and fine-tuning spot colors.

## Slide 7: ECG Reference Profiles
ICC Profile
inks | samples
4 | 1617
5 | 10254
6 | 65023
7 | 412328
Notes: Slide 7 – ECG Reference Profiles – TIMING 1.5 MINUTES
As Chuck explained, the targeted printing process is described by an ICC printer profile. So, let’s start with that.
Usually, this is a standard profile such as GRACoL or SWOP. There may soon be standard ECG profiles for flexo (nod to Steve). It could also be a profile of your own printing process.
According to the ICC standard, printer profiles may have up to 15 ink channels, but there are practical limitations.
The Optimal Method uses a ”forward” tag to transform %-dot values to L*a*b* values.
The size of this tag increases exponentially with the number of inks.
[change slide]
A test chart with 1617 samples is commonly used to make a CMYK profile. To achieve the same resolution, a 7/C profile would need over 400,000 samples!
In practice, a 7/C profile might be built from 4,000 samples, which is just 1% of the number required for CMYK-level resolution.
Profiles made from these “sparse” data sets must estimate the missing information. This may reduce their accuracy.

## Slide 8: Statistically Accurate Calibration
trendline
y = x + random
Notes: Slide 8 – Statistically Accurate Calibration – TIMING 1.5 MINUTES
Despite the relative inaccuracy of ECG profiles, color transforms using them are completely repeatable.
Furthermore, we can make a statistically accurate snapshot of the printing process with a well-chosen sample set.
The Optimal Method calibrates to this snapshot, rather than to individual samples.
For example, here is a graph of 21 samples with +/- 5% random variation.
A trendline, fitted to these samples using least squares, matches the underlying function (y = x) within +/- 0.1%.
By using an abundance of samples, we can separate the underlying function from the variation.
The Optimal Method works like this, except there are multiple dimensions (inks), and the trendlines are tone curves.
This is why Optimal Method calibrations are statistically accurate, even with sparse reference profiles and rough measurements. We like to say, “The Optimal Method is robust.”

## Slide 9: Choosing Samples for Calibration
ICC Profile
B2A1 Tag
“Realistic” Colors
L*a*b*
CMYKOGV
Notes: Slide 9 – Choosing Samples for Calibration – TIMING 1 MINUTE
Calibration involves printing and measuring a test chart containing color samples.
There are various beliefs about which color samples should be used, as Chuck explained earlier.
We recommend a sample set containing a full range of colors you’re likely to print.
Most of these colors are derived from an ICC printer profile, at some stage in design or prepress.
The combinations of inks that produce a given color are embedded in the ”reverse” tags of the printer profile.
A set of L*a*b* values (on the left) is transformed to CMYKOGV values (on the right).
We call these “realistic” colors.
Optimal curves built using “realistic” color samples will produce the best results.

## Slide 10: PressCal Test Chart Tool
CMYK Ramps
Gray Ramps
OGV Ramps
“Realistic” Samples
(CMYKOGV)
“Realistic” samples in L*a*b* color space
Notes: Slide 10 – PressCal Test Chart Tool – TIMING 0.8 MINUTES
We’ve developed a free tool to make ECG test charts containing these “realistic” color samples.
The samples are derived from the reference profile, which may have any number of ink channels.
Here is an example test chart, made from a CMYKOGV profile.
There are process and gray ramps at the top of the chart followed by the realistic samples at the bottom.
[change slide]
Here is a 3-D view of the realistic samples, which are distributed uniformly throughout the color gamut.

## Slide 11: Making ECG Tone Curves
Notes: Slide 11 – Making ECG Tone Curves – TIMING 1.5 MINUTES
To make tone curves, print and measure the PressCal test chart.
[change slide]
Open the “Extended Gamut” basic settings file, which is a template for this task.
[change slide]
Enter paths to your reference profile and measurements.
[change slide, movie is 56 secs long]
Run the curve building tool.
Initial color errors are displayed, followed by curve optimization.
The computed curves are displayed in the web browser along with cumulative error distributions, before and after.
The residual color errors of the individual samples are displayed.
Curves are saved to the desktop – in this case, tab delimited and ISO 18620.
Here is the contents of the tab-delimited table.
Because we used a full range of realistic color samples, individual ink variations and their interactions are accounted for.

## Slide 12: Color Errors Are Reduced
Before (uncalibrated)
After (curves applied)
1.80 ∆E00
0.80 ∆E00
Notes: Slide 12 – Color Errors Are Reduced – TIMING 0.8 MINUTES
The cumulative error distribution is a good indicator of the color match.
In this example, the median color error was reduced from 1.8 to 0.8 ∆E00.
That is a big improvement!
For reference, a freshly profiled ink jet proofing system might have a median error of 0.5 ∆E00.
When compared to other calibration methods, the Optimal Method will always have the lowest residual color error.

## Slide 13: Applying Curves
token | output format | file type | colors | steps
apogee | Agfa Apogee | XML | CMYK | Y
cgats | CGATS.17 text format | text | n-color | Y
device_link | ICC device link profile | binary | n-color | N
efi | EFI XF .vpc/.vcc | text | CMYK + 4 spot | Y
equios | DS Equios | text | CMYK | N
fuji_xmf | Fuji XMF | text | CMYK | N
harlequin | Harlequin-based RIP | text | CMYK | N
heidelberg | Prinect (CTS 2.1, measured or calibration) | text | CMYK | Y
hybrid | Hybrid PACKZ | JSON | n-color | Y
indigo | HP Indigo | text | CMYK | N
iso_18620 | ISO 18620 (Esko .ted) | XML | n-color | Y
navigator | Xitron Navigator (push calibration) | Postscript | n-color | N
photoshop | Photoshop .acv | binary | n-color | Y
prinergy | Kodak Prinergy Harmony (Colorflow) | text | CMYK | N
process | process control report (details) | text | n-color | Y
rampage | Rampage curve set | text | CMYK | N
sierra | Xitron Sierra | text | CMYK | N
trueflow | Screen Trueflow | binary | CMYK | N
text | tab-delimited text | text | n-color | Y
Notes: Slide 13 – Applying Curves – TIMING 0.7 MINUTES
Once curves are computed, the next step is to enter them into your prepress workflow.
PressCal can output curves in many file formats to simplify this task.
[change slide]
Here is a table of 18 supported curve formats.
If you need a format that’s not listed, let us know. We will try to add it.
If you’re using a color-managed workflow, PressCal can apply curves to ICC profiles.
So, both conventional and digital presses can be calibrated using our tools.

## Slide 14: Spot Color Simulation
Notes: Slide 14 – Spot Color Simulation – TIMING 0.5 MINUTES
The main reason for adopting an ECG process is the simulation of spot colors.
Spot colors are replaced by process color mixes, which avoids using spot color inks, and simplifies production.
For this to work, spot colors must lie within the gamut of the ECG process.
The process color mixes must then be determined with good accuracy.
Spot color matching is generally more critical than pictorial color.

## Slide 15: Adding Spot Color Mixes to the Calibration Chart
Spot Colors
Notes: Slide 15 – Adding Spot Color Mixes – TIMING 0.8 MINUTES
The test chart tool allows you to add spot color mixes to the calibration chart.
There are various ways to specify the colors, including L*a*b* values, spectral measurements, CxF/X-4, and color book names.
Here is an example using some Pantone colors. Any number of spot colors may be added.
[change slide]
Notice that some of the colors are marked “out-of-gamut”. It may be necessary to handle these as real spot colors, if the color error is too large.
[change slide]
The spot colors are appended to the test chart and measured along with the other calibration samples.

## Slide 16: Color Management May Not Be Accurate Enough for Spot Colors
“Eyeball” spot color changes
Notes: Slide 16 – Color Management May Not Be Accurate – TIMING 1 MINUTE
As mentioned earlier, ECG profiles may be inaccurate when calculating individual colors.
Changes in the printing process may also cause spot colors to be inaccurate, even after calibration.
Brand colors are often the most critical colors in a job.
So, computed color mixes from a reference profile may not meet your customer’s requirements.
[change slide]
This Is evident from the existence of tools to fine-tune spot colors visually, by printing a range of variations to select from.
While this is a reasonable approach for digital printing, it is impractical for conventional presswork, or when there are many colors to “tweak.”

## Slide 17: PressCal Spot Color Tool
Compares L*a*b* values
Adjusts CMYKOGV values
Notes: Slide 17 – PressCal Spot Color Tool – TIMING 0.8 MINUTES
So, we developed another tool to fine-tune spot color mixes.
This tool compares the spot color measurements from the calibration chart with the target color values.
[change slide]
It then adjusts spot color mixes using the reference profile.
Note, the colors shown here are “realistic”, for compatibility with pictorial content.
Spot color mixes may also be computed using just 3 inks. Two alternate algorithms are provided, one favoring CMY inks and the other favoring non-CMY inks.

## Slide 18: Improved Spot Color Accuracy
Notes: Slide 18 – Improved Spot Color Accuracy – TIMING 0.5 MINUTES
Although the initial colors may have been inaccurate, the adjusted colors will be surprisingly close.
[change slide]
This is possible because the ICC reference profile tells us how to make fine adjustments from the initial measured color.
The tool supports multiple iterations for further improvement, but a single adjustment is usually sufficient.

## Slide 19: Tone Curves and Spot Color Mixes from a Single Test Run!
Tone Curves
Spot Color Mixes
Free?
What’s the catch?
Notes: Slide 19 – Tone Curves and Spot Color Mixes – TIMING 1.6 MINUTES
We’ve demonstrated building ECG tone curves with the Optimal Method.
We’ve also demonstrated new tools to generate ECG test charts and fine-tune spot color mixes.
With these tools, you can calibrate your ECG system and build accurate spot color mixes from a single test run!
[change slide]
PressCal is open source software.
It is licensed under the General Public License, version 3. As the logo says, it is “free as in freedom.”
This means you’re free to modify and distribute it, as you see fit.
There is a document on our web site explaining how to modify PressCal.
[change slide]
It is also “free as in gratis”. You can download it from our web site and have it working in a few minutes.
[change slide]
I don’t know about you, but whenever I hear something is free, I think “What’s the catch?”
If you read our article in “Flexo” magazine, you already know the Optimal Method was born from our standards and consulting work.
This work provides the motivation, resources, and ideas for improving our tools.
So, the catch is, “Your consulting business pays for the free software.”
Thank you for your attention.

## Slide 20: Thank You!
Charles (Chuck) Spontelli Bowling Green State University csponte@bgsu.edu
William (Bill) B. Birkett Doppelganger, LLC wbirkett@doplganger.com
Web Site https://optimalmethod.org